## Slide 1: Experiment AU46-PMC-AU1: detectability of Non-acetylated K122-MnSOD peptide

## Slide 2: Experiment AU46-PMC-AU1
Following concentrations of non acetylated K122-MnSOD were run on HPLC to see the detection limit- 10, 5, 2.5, 1.25, and 0.625 uM on two different days with each as fresh samples (Inter-day).
Each inter-day samples were re-run for intra-day repeat.
I assumed these non acetylated K122-MnSOD will represent 10% product formation which will be converted in to substrate. The corresponding substrate concentration will be 100, 50, 25, 12.5, and 6.25 uM.
A reaction will be carried out to confirm the above assumption (PMC-AU2c, d) starting with 6.25 uM substrate concentration. If the expected product formation is below the area reported in this, then I will choose next high concentration e.g. 12.5 uM.
Please see attached raw and final data in excel sheet and screen shots in next slides.
I have compared data from both auto (software) and manual integration.

## Slide 3
Day 1 and Day 2 represents inter-day repeats to each other; run 1 and run 2 in same day represents intra-day repeats.
Auto integration |  |  |  |  |  | 
assume 10% product formed |  | Day 1 (comparing intra-day of day 1) |  |  |  | 
[product] uM | [product] pmole | Run 1 | Run 2 | Average | SDEV | % CV
0.625 | 25 | 25.35 | 17.21 | 21.28 | 5.755849 | 27.05
1.25 | 50 | 43.02 | 50.15 | 46.585 | 5.041671 | 10.82
2.5 | 100 | 102.9 | 114.97 | 108.935 | 8.534779 | 7.83
5 | 200 | 227.54 | 220.67 | 224.105 | 4.857824 | 2.17
10 | 400 | 447.16 | 465.06 | 456.11 | 12.65721 | 2.78
assume 10% product formed |  | Day 2 (comparing intra-day of day 2) |  |  |  | 
[product] uM | [product] pmole | Run 1 | Run 2 | Average | SDEV | % CV
0.625 | 25 | 23.15 | 25.32 | 24.235 | 1.534422 | 6.33
1.25 | 50 | 48.7 | 44.4 | 46.55 | 3.040559 | 6.53
2.5 | 100 | 103.34 | 91.27 | 97.305 | 8.534779 | 8.77
5 | 200 | 197.8 | 197.99 | 197.895 | 0.13435 | 0.07
10 | 400 | 426.75 | 414.4 | 420.575 | 8.732769 | 2.08
assume 10% product formed |  | Day 1 and 2 (comparing inter-day of two day experiment) |  |  |  | 
[product] uM | [product] pmole | Area-Run1-Day 1 | Area-Run1-Day 2 | Average | SDEV | % CV
0.625 | 25 | 25.35 | 23.15 | 24.25 | 1.555635 | 6.41
1.25 | 50 | 43.02 | 48.7 | 45.86 | 4.016367 | 8.76
2.5 | 100 | 102.9 | 103.34 | 103.12 | 0.311127 | 0.30
5 | 200 | 227.54 | 197.8 | 212.67 | 21.02936 | 9.89
10 | 400 | 447.16 | 426.75 | 436.955 | 14.43205 | 3.30

## Slide 4
Manual integration |  |  |  |  |  | 
assume 10% product formed |  | Day 1 (comparing intra-day of day 1) |  |  |  | 
[product] uM | [product] pmole | Run 1 | Run 2 | Average | SDEV | % CV
0.625 | 25 | 16.38 | 16.11 | 16.245 | 0.191 | 1.18
1.25 | 50 | 42.37 | 43.58 | 42.975 | 0.856 | 1.99
2.5 | 100 | 96.68 | 91.65 | 94.165 | 3.557 | 3.78
5 | 200 | 210 | 206.27 | 208.135 | 2.638 | 1.27
10 | 400 | 424.29 | 429.886 | 427.088 | 3.957 | 0.93
assume 10% product formed |  | Day 2 (comparing intra-day of day 2) |  |  |  | 
[product] uM | [product] pmole | Run 1 | Run 2 | Average | SDEV | % CV
0.625 | 25 | 20.35 | 19.8 | 20.075 | 0.389 | 1.94
1.25 | 50 | 41.9 | 43.75 | 42.825 | 1.308 | 3.05
2.5 | 100 | 88.69 | 85.49 | 87.090 | 2.263 | 2.60
5 | 200 | 179.98 | 179.97 | 179.975 | 0.007 | 0.00
10 | 400 | 400.66 | 391.5 | 396.080 | 6.477 | 1.64
assume 10% product formed |  | Day 1 and 2 (comparing inter-day of two day experiment) |  |  |  | 
[product] uM | [product] pmole | Area-Run1-Day 1 | Area Run1--Day 2 | Average | SDEV | % CV
0.625 | 25 | 16.38 | 20.35 | 18.365 | 2.807 | 15.29
1.25 | 50 | 42.37 | 41.9 | 42.135 | 0.332 | 0.79
2.5 | 100 | 96.68 | 88.69 | 92.685 | 5.650 | 6.10
5 | 200 | 210 | 179.98 | 194.990 | 21.227 | 10.89
10 | 400 | 424.29 | 400.66 | 412.475 | 16.709 | 4.05