## Slide 1: Objective: To develop a standardised method for measuring annealing/ melting rates for complementary DNA oligomers by UV absorbance spectroscopy.
Briefly,
  Complementary oligomers are mixed together in a standard buffer in equal molarity.
  Both ssDNA and dsDNA concentration is measured at 260nm. During a melt run, as temperature is increased, absorbance(260nm) increases with increasing single-stranded DNA. Alternatively, as temperature is decreased, absorbance(260nm) decreases with decreasing single-stranded DNA.
  Thus the absorbance at any instant of time in a thermal (melt) run can be correlated to the ds/ ss DNA concentration at that instant by using the absorbance at 25oC (when the oligos are completely annealed or ds) or using the absorbance at 90oC (when the oligos are completely melted or ss form) respectively.
  To determine the rate of annealing/ melting at any given temperature, two approaches have been tried:
    The complementary oligomers are cooled from 90oC to the hold temperature being tested, say, 70oC. The ramp down rate and hold time are known (and user programmed). Once at the desired temperature, the sample is incubated for a prolonged period of time so that the change in absorbance over time can be monitored in real time.
    the complementary oligomers are heated from 60oC to the temperature being tested, say 70oC. The ramp-up rate and the hold time are known (and user programmed). Once at the desired temperature, the sample is incubated for a prolonged period of time so that the change in absorbance over time can be monitored in real time.
  The data in the following slides used the first protocol ie Prcl 1.

## Slide 2: Oligomer details
Name | Size | Sequence | %GC | Melting Temperature, Tm* (width/ range of melting)
A1a16 | 40bases | 5’- GACTGCAAAGATGGAAACGACCTTCTATGACGATGCCCTC-3' | 50 | 77oC (3oC)
A2 (complementary oligo) | 40bases | 5'-GAGGGCATCGTCATAGAAGGTCGTTTCCATCTTTGCAGTC-3' | 50 | 
*: This is the melting temperature in the absence of any dye |  |  |  | 
Melt Curve of oligo pair A1a16-A2 performed as part of this experiment (also in the absence of dye)
First derivative of the melt curve of A1a16-A2, the positive peak represents the melting temperature (Tm = 77oC, see table above).
Second derivative of the melt curve of A1a16-A2, the positive and negative peaks represent the limits of the range of temperatures over which melting occurs (width = 3oC, see table above); the point at which the plot cuts the X-axis is the Tm (77oC).
Chart: Temperature (oC)
75.02
78.02

## Slide 3: Methods: Protocol 1 The experiment is carried out in the Cary 100 UV-Vis Spectrophotometer
Reaction Sample prepared as follows:
Reaction sample denatured as follows (program used is denat mthd 2):
  Heated up to 95oC at 10oC/min
  Held at 95oC for 1.5min
  Returned to 90oC
Reaction sample subjected to melt - kinetic run at desired temperature (74/ 75/ 76oC) (program used is prcl1 mthd 1).
Protocol 1 Mthd 1 details:
  Start thermal run at high end (90oC)
  Ramp down to desired temperature (74/ 75/ 76oC) for thermal (melt) profile
  Hold at desired temperature for kinetic run until equilibration
  See following slide for instrument parameters
Component | Source | Concentration
Native Taq Polymerase buffer | Life Technologies | 1X
MgCl2 | Life Technologies | 2mM
Oligo 1 (A1a16) | Sigma Custom Oligos | 1uM
Oligo 2 (A2) | Sigma Custome Oligos | 1uM
Total vol |  | 1500ul

## Slide 4: Comparison of melting kinetics of A1a16-A2 oligo pair (40bp, %GC = 50) at 74-75-76-78oC as measured by UV absorbance spectroscopy
Thermal (melt) run from 90 to 74/ 75/ 76/ 78oC
Kinetic run at 74/ 75/ 76/ 78oC for 120secs*
*See following slide for scale up of kinetic plots
Thermal Run Instrument Parameters |  |  | 
Start Temp |  | 90oC | 
End Temp |  | 74/ 75/ 76oC | 
Ramp Rate |  | 0.5oC/min | 
Avg Time |  | 2sec | 
Data Interval |  | 1oC | 
Kinetic Run Instrument Parameters | 
Stop Time | 2min
Signal Averaging Time (SAT) | 0.1secs
Data Interval | 1sec
Chart: temp (oC)
| 89.91999817 | 89.019996640000016 | 87.97000122 | 86.97000122 | 86.019996640000016 | 84.980003359999998 | 83.91999817 | 83.019996640000016 | 81.97000122 | 81.069999690000017 | 79.97000122 | 79 | 77.97000122 | 77.069999690000017 | 76.019996640000016 | 75.019996640000016 | 73.97000122
1uM oligo 90-74oC | 1.0767 | 1.0733 | 1.0744 | 1.0727 | 1.0733 | 1.0722 | 1.0712 | 1.073 | 1.0729 | 1.0705 | 1.0686 | 1.0618 | 1.0401 | 1.0052 | 0.9774 | 0.95294 | 0.9376
1uM oligo 90-75oC | 0.88751 | 0.88647 | 0.8882 | 0.88875 | 0.88879 | 0.88908 | 0.8893 | 0.88945 | 0.8886 | 0.8877 | 0.88328 | 0.87401 | 0.84945 | 0.81774 | 0.78613 | 0.7657
1uM oligo 90-76oC | 1.0871 | 1.0948 | 1.0959 | 1.0975 | 1.0943 | 1.0978 | 1.0968 | 1.0964 | 1.0955 | 1.0931 | 1.089 | 1.0779 | 1.0554 | 1.0199 | 0.99232
1uM oligo 90-78oC | 0.91743 | 0.91608 | 0.91591 | 0.91551 | 0.91524 | 0.91552 | 0.91512 | 0.91445 | 0.91305 | 0.91213 | 0.91008 | 0.90171 | 0.87801
Chart: time (secs)

## Slide 5: Scale up of Kinetic Plots for A1a16-A2 at 74-75-76-78oC to view the trend of the first 5secs and the first 20secs
Chart: time (secs)
Chart: time (secs)
Chart: time (secs)
Chart: time (secs)
Chart: time (secs)
Chart: time (secs)
Chart: time (secs)
Chart: time (secs)
Chart: time (secs)
Kinetic run at: 74oC 75oC 76oC 78oC
0secs -120secs
0secs -5secs
0secs -20secs
A(260nm)
Chart: time (secs)
Chart: time (secs)
Chart: time (secs)

## Slide 6: Summary of results
Both ssDNA and dsDNA concentration is measured at 260nm. During a melt run, as temperature is increased, absorbance(260nm) increases with increasing single-stranded DNA. Alternatively, as temperature is decreased, absorbance(260nm) decreases with decreasing single-stranded DNA.
As expected, as the end temperature of the melt run is increased from 74 to 78oC, the D absorbance increases (see below). Also as kinetic run temperature is increased from 74 to 76oC, the D absorbance at the end of 2mins increases. There is a trend from 74 to 76oC, however the increase is not very significant.
The temperatures chosen for this experiment were based on the Tm of the ds oligo complex in the absence of dye (~77oC).
Also, please note last 2 columns of kinetic run (bordered in black): These show the distinct trend in the first 5 secs which is temperature dependent. This can also be seen in the plots in the previous slide.
Expt end (kinetic run) temp | Thermal run |  |  | Kinetic run |  |  |  | 
 | Absorbance[start] (90oC) | Absorbance[end] (74/ 75/ 76oC) | Dabsorbance = A(end) – A (start) | Absorbance[start] (t=0) | Absorbance[end] (t=120) | Dabsorbance = A(end) – A (start) | Absorbance (t=5) | Dabsorbance = A(t=5) – A (t=0)
74oC | 1.0767 | 0.9376 | -0.1391 | 0.9359 | 0.9393 | 0.0033 | 0.9322 | -0.0037
75oC | 0.8875 | 0.7657 | -0.1218 | 0.7646 | 0.7706 | 0.0059 | 0.7643 | -0.0003
76oC | 1.0871 | 0.9923 | -0.0948 | 0.9892 | 0.9986 | 0.0094 | 0.9916 | 0.0024
78oC | 0.9174 | 0.8780 | -0.0394 | 0.8799 | 0.8804 | 0.0005 | 0.8809 | 0.0010